## Slide 1: Mid-term Präsentation HW/SW Co-Design LU
Andreas Dejmek 01325347
Stefan Huemer 01027799

## Slide 2: Task idea
Direct FIR
FDL Header
FDL Body
FFT- Header
FFT- Body
Input
Output
512 Samples
256 Samples
4096 Samples
Double-FDL Convolution

## Slide 3: N-taps FIR-Filter
x(n-1)
x(n)
x(n-2)
x(n-N-2)
x(n-N-1)
b0
b1
b2
bN-1
bN
…
…
…
Input
Output

## Slide 4: N-taps FIR-Filter
Latency: 4 cycles
 N = 512 Samples
Problem: 511 Multipliers needed
Board only has 266 Multipliers

## Slide 5: New FIR-Filter idea
FIFO /
On-Chip Memory
Input
FIFO /
On-Chip Memory
Coefficients
FIR
.
Only one
MAC / cycle

## Slide 6: FFT
Idea: Using IP core
  Altera Fast Fourier Transform II Ver. 18.1
Needs Bus wrapper to work with Nios II

## Slide 7: Memory options
SRAM
  2 MB (2.097.152 bytes)
  16-bit wide entries
  max. 125 MHz
Access time
  read: 2 cycles / (1 cycle possible?)
  write: 1 cycle

## Slide 8: Memory options
SDRAM
  128 MB
  32-bit wide entries
  max. 100 MHz
Access time
  read: 1 cycle
  Refresh (worst case 1 cycle 80% of time)

## Slide 9: Memory options
Tightly coupled memories (On-chip RAM)
  Size dependent on free space on PL
  custom width entries
Access time
  read: 1 or 2 clock cycles

## Slide 10: Memory usage
FIFO/On-chip RAM
  Input signal 4096 samples
  h0 (512-bits) for FIR
  Buffer
SRAM
  H1 – H14 (transformed)
  X0 – X-13 (transformed)
SDRAM
  H15 – H38 (transformed)
  X0 – X-22 (transformed)
  Output signal (for 2nd mode)

## Slide 11: Memory requirement
256 block size (header)
* 2 zero extended blocks (frequency domain)
* 14 (number of blocks)
* 2 stereo
* 32 (bit width)
* 2 real / imaginary
* 2 ( for H / X)
 1.835.008 bits ≙ 229.376 bytes

## Slide 12: Memory requirement
4096 block size (body)
* 2 zero extended blocks (frequency domain)
* 23 (number of blocks)
* 2 stereo
* 32 (bit width)
* 2 real / imaginary
* 2 ( for H / X)
 48.234.496 bits ≙ 6.029.312 bytes
SRAM to small

## Slide 13: Accuracy
Stereo value 16 bits each
After FFT  32 bits real / imaginary
After Multiply  64 bits real /imaginary
After Add  65 bits real /imaginary
Trim value before or after IFFT?

## Slide 14: Timing
48 kHz Sampling frequency
100 MHz clock
 new sample every 2080 cycles

## Slide 15: Timing requirement
FIR
  2080 cycles
FFT-Header
  532.480 cycles
FFT-Body
  8.519.680 cycles
Bottleneck
  Memory read for multiplication

## Slide 16: Timing requirement
FIR
  No problem
FFT-Header
  SRAM requires 4 access / sample
  Access time 1 cycle
  Requires 458.752 of 532.480 cycles
  73.728 cycles for other operations
FFT-Body
  SDRAM requires 2 access / sample
  Access time 1,2 cycles
  Requires 3.617.588 of 8.519.680 cycles
  4.902.092 cycles for other operations

## Slide 17: Algorithm
Currently implement in matlab script
Next step:
  C program
  Using hardware components

## Slide 18: Thank you for your attention!
Questions?