## Slide 1: Mid-term Präsentation HW/SW Co-Design LU
Andreas Dejmek 01325347
Stefan Huemer 01027799

## Slide 2: Task idea
Direct FIR
FDL Header
FDL Body
FFT- Header
FFT- Body
Input
Output
512 Samples
256 Samples
4096 Samples
Double-FDL Convolution

## Slide 3: N-taps FIR-Filter
x(n-1)
x(n)
x(n-2)
x(n-N-2)
x(n-N-1)
b0
b1
b2
bN-1
bN
…
…
…
Input
Output

## Slide 4: N-taps FIR-Filter
Latency: 4 cylces
 N = 512 Samples
Problem: 511 Multipliers needed
Board only has 266 Multipliers

## Slide 5: New FIR-Filter idea
FIFO /
On-Chip Memory
Input
FIFO /
On-Chip Memory
Coefficients
FIR
.
Only one
MAC / cycle

## Slide 6: FFT
Idea: Using IP core
  Altera Fast Fourier Transform II Ver. 18.1
Needs Bus wrapper to work with Nios II

## Slide 7: Memory options
SRAM
  2 MB (2.097.152 bytes)
  16-bit wide entries
  max. 125 MHz
Access time
  read: 2 cycles
  write: 1 cycle

## Slide 8: Memory options
SDRAM
  128 MB
  32-bit wide entries
  max. 100 MHz
Access time
  read: 5,5 ns

## Slide 9: Memory options
Tightly coupled memories (On-chip RAM)
  Size dependent on free space on PL
  custom width entries
Access time
  read: 1 or 2 clock cycles

## Slide 10: Memory usage
Input signal
  4096 deep memory in FIFO/On-chip RAM
Impulse response
  h0 (512-bits) for FIR in FIFO/On-chip RAM
  H1 - Hn (transformed) in SRAM
Output signal (for 2nd mode)
  saved in SDRAM

## Slide 11: Timing
48 kHz Sampling frequency
100 MHz clock
 new sample every 2080 cycles

## Slide 12: FFT-Header
14 blocks with 256 samples each
result has to be computed after 256 samples or 532.480 cycles

## Slide 13: FFT-Header
Calculating header blocks requires
  1 cycle for saving new x
  256 cycles for FFT ( x  X )
  for each block
    512 cycles for reading Hn ( read from SRAM is 2 cycles )
    ?? cycles for multiplication ( X * Hn )
    1 cycle for accumulation
  512 cycles for IFFT ( X  x )

## Slide 14: FFT-Header
This has to be done for 14 header blocks two times (stereo)
Assuming 500.000 cycles time for the multiplication
(256 * 14 * 2) * x = 500.000 => x ≈ 69 cycles time for each multiplication

## Slide 15: FFT-Body
23 blocks with 4096 samples each
result has to be computed after 4096 samples or 8.519.680 cycles

## Slide 16: FFT-Body
Calculating body blocks requires
  1 cycle for saving new x
  4096 cycles for FFT ( x  X )
  for each block
    8192 cycles for reading Hn ( read from SRAM is 2 cycles )
    ?? cycles for multiplication ( X * Hn )
    1 cycle for accumulation
  8192 cycles for IFFT ( X  x )

## Slide 17: FFT-Body
This has to be done for 23 body blocks two times (stereo)
Assuming 8.400.000 cylces time for the multiplication
(4096 * 23 * 2) * x = 8.400.000 => x ≈ 44 cycles time for each multiplication

## Slide 18: FFT - Bottleneck
Calculating FFT-Header and FFT-Body at the same time
According to estimates one FFT-Body can be finished after one FFT-Header was calculated

## Slide 19: Thank you for your attention!
Questions?